## Slide 1: Mapping Circuit Fault diagnosis problems
Brad Lackey
Microsoft Quantum
Bian, et al., Frontiers in Physics 2:56, 2014.
Bian, et al., Frontiers in ICT 3:14, 2016.
Perdomo-Ortiz, et al., Phys. Rev. Appl. 12:1, 2019.
Notes: We won’t be talking about hardware or algorithms to solve binary problems, or even benchmarking circuit fault diagnosis problems.
Rather we will only discuss how to create (in some sense optimal) Ising models that capture solving this problem, and by extension other similar problems.
There is literature benchmarking a variety of binary solvers (including quantum annealers) on circuit fault diagnosis problems.
Naturally, there is a huge literature on methods of for solving diagnosis problems in general.

## Slide 2: Circuit Fault Diagnosis Problems

## Slide 3: Fault diagnosis is widely studied
Fault Diagnosis is a broad topic
We will focus on hardware circuits
DX (Principles of Diagnosis workshop)
33Rd Annual Was in TOULOUSE (2022)
Named application in several programs
IARPA QEO
Darpa QAFS and Quicc
Benchmark libraries
ISCAS 85, iscas 89, and ITC 99.

## Slide 4: Consider a Circuit For example, a full-adder
X1
X2
A1
A2
O1
XOR gates
AND gates
OR gate
Suppose we have a Large circuit
There are many components
Connected by a complex network
Broken gate
But some of the components are Faulty
Strong model: they break in predictable ways
Weak model: we don’t care how they break
How do we find what broke?

## Slide 5: Circuit Fault diagnosis Provide test vectors, make observations
X1
X2
A1
A2
O1
WE are provided test vectors:
Inputs (1,0,1) produce outputs (0,1).
Now make observations:
What does the circuit compute on the inputs?
(Minimal Cardinality) Fault Diagnosis:
  Find the least number of Faults
  That explain the observation.
0
1
1
1
0
1
0
0
0
1
1
1
Stuck-at-zero
Both outputs are incorrect
1
0
0
0
Notes: Setting the state for the problem: we have a dictionary of input/output test vectors to check whether a design conforms to the desired behaviors.
If it does not (as in the case shown here), there are at least one components of the circuit that are unhealthy.
Imagining that component errors happen independently with low frequency, the most likely diagnoses are those where a minimum number of components in a fault mode.
For small examples, such as the one here, we can solve these by hand with a bit of reasoning (figure out where the faulty components must lie based on which outputs are wrong). If we were in the weak fault model, we would are done: we found a faulty component that explains the output. In the strong fault model, however, we would question if how our component breaks is compatible with what we expect.

## Slide 6: Circuit Fault Diagnosis Strong Fault model
We can have multiple models of behavior.
Healthy: the component behaves correctly.
Faulty: The component fails predictably.
X1
X2
A1
A2
O1
XOR>SA0(X1)
Broken it’s stuck-at-zero
Healthy it’s XOR
Notes: This is (simplification) of what would find in standard EDA, almost.
In our behaviors we specifically note that if a gate is health (not in error), then it obeys standard logic.
Fault diagnosis adds fault behaviors to gates.
We focus on two very simple faults, “stuck-at” faults, where the gate always outputs the same value irrespective of its inputs.
One could envision many other kinds of faults.
For our purposes here we require the faults to be deterministic: if a gate is at fault, it always behaves the same way (i.e. not randomly).

## Slide 7: Hamiltonian Synthesis

## Slide 8: Example: a Nand gate Healthy behavior
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
out | A | B
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 0
0 | 0 | 1
1 | 0 | 1
0 | 1 | 1
1 | 1 | 1
out | A | B
1 | 0 | 0
1 | 1 | 0
1 | 0 | 1
0 | 1 | 1
Let’s start with the truth table for a Nand gate.
Issue: when we have faults Inputs and outputs may be wrong.
Instead let’s list the “good” versus “bad” configurations.
We distinguish good and bad configurations with a penalty.
Good configurations receive no penalty.
Bad Configurations get the full penalty.

## Slide 9: Example: a Nand gate Healthy behavior
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
We want to capture the penalty with a formula.
These are often called “pseudo-Boolean” functions.
They have bits as inputs but real values as outputs.
Standard mathematical trick for this: “Lagrangian interpolation.”
For pseudo-Boolean functions this always give a polynomial
Ouch! A degree 3 term.

## Slide 10: Example: a Nand>SA1 gate Healthy behavior
Consider Our “NAnd” gate, with a stuck-at-one fault.
Four States belong to the healthy behavior.
  These receive a penalty of zero.
Three States are incompatible with the gate.
  These receive a penalty of one.
Now One State represents the valid fault Behavior.
  We Give this a “small” penalty.
Again, Lagrangian interpolation gives a Polynomial.
It’s a bit messy so I won’t print it here.
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
Notes: To add a fault mode, there are two approaches.
The minimum one, is to directly insert the error behavior into the truth table of the circuit.

## Slide 11: Hamiltonian synthesis General ideas
IN summary:
Healthy behaviors have no penalty
Faulty Behaviors have a small penalty
Infeasible states have a large Penalty
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
Healthy behaviors
Faulty behaviors
Infeasible states
For large circuits
Sum up the penalties of its components
X1
X2
A1
A2
O1

## Slide 12: Hamiltonian Synthesis Adding Observations
X1
X2
A1
A2
O1
0
1
1
0
1
0
1
We have not accounted for Observations
Add A Penalty if the output does not agree
Healthy Behavior now has a Penalty
The Diagnosis with Fewest faults Has the lowest Penalty
Finding the Lowest penalty solves the Diagnosis Problem.
Notes: Mapping a circuit fault diagnosis problems into a binary optimization problem is somewhat abnormal.
Ordinarily we would view the ground state as the desired solution we aim to find, and this will eventually be true.
However, to set up the problem we need address healthy behavior versus faulty behavior (on a graded scale by cardinality) versus configurations simply do not represent any way that the circuit operates.
Then, we encode our observations by adding a penalty to a configuration incompatible with what we observe on the given wires.
This pushes behaviors incompatible with the observation into excited states.
What is left as ground states are the (fault) behaviors compatible with the observations.

## Slide 13: Reducing degree

## Slide 14: Hamiltonian Synthesis Desirable and Undesirable Features
Let’s Revisit our “NAnd” gate:
Our “Gap” is large (good)
  We have more room to insert Fault penalties
  Physics-based optimizers want a large spectral Gap
Our coefficients are not really big (Good)
Our Penalty function is cubic (Bad)
  Physical systems typically do not have strong many-body interactions
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
Notes: First consider describing the healthy behavior of a nand-gate.
Doing the most mathematically accessible mapping produces a cubic PUBO (and corresponding “third-order” Ising model).
There are standard methods to reduce to a QUBO (correspondingly a Ising model).

## Slide 15: Hamiltonian Synthesis Reducing Degree
There is a standard tricks to reduce degree:
Introduce an extra bit
We’ll do something different.
out | A | B | P
0 | 0 | 0 | 1
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
out | A | B | P
0 | 0 | 0 | 3
1 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 1
Notes: First consider describing the healthy behavior of a nand-gate.
Doing the most mathematically accessible mapping produces a cubic PUBO (and corresponding “third-order” Ising model).
There are standard methods to reduce to a QUBO (correspondingly a Ising model).

## Slide 16: Hamiltonian Synthesis Searching for Penalties
How did we know To set that penalty to three?
Don’t start with the penalties, start with polynomial
Now it’s guaranteed to have the right degree
  We have to maximize the least penalty
  We can’t the coefficients of P get Large
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
Notes: First consider describing the healthy behavior of a nand-gate.
Doing the most mathematically accessible mapping produces a cubic PUBO (and corresponding “third-order” Ising model).
There are standard methods to reduce to a QUBO (correspondingly a Ising model).

## Slide 17: Gap Optimal Hamiltonians

## Slide 18: Hamiltonian Architecture
An architecture is A space of polynomials with coefficient bounds
Healthy behaviors gives equations for our coefficients:
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
Notes: Really, an architecture is just a selection of bounds in our Hamilton coefficients.
We require the zero Hamiltonian be in any architecture for technical reasons.
Ising models, with a given interaction graph, can be specified by setting coefficient not supported by the model to zero.

## Slide 19: Gap Optimal Hamiltonians
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
out | A | B | P
0 | 0 | 0 | 
1 | 0 | 0 | 0
0 | 1 | 0 | 
1 | 1 | 0 | 0
0 | 0 | 1 | 
1 | 0 | 1 | 0
0 | 1 | 1 | 0
1 | 1 | 1 | 
Otherwise, we want to maximize the Gap (smallest penalty)
That is: maximize Such that

## Slide 20: Linear Programming
Finding the gap optimal Hamiltonian for an architecture a linear program.
For our NAND gate: maximize Such that
There is standard Software that can solve these efficiently.
Notes: Expanding out the formula for a generic Hamiltonian shows that finding a gap-optimal Hamiltonian is a linear program.
The notation here can be a bit daunting. Recall:
The s^I terms means the function that multiplies the spin values at the indices contained the set I.
The C_I are the coefficients of the Hamiltonian, which are the variables of the linear program.
And finally, gamma is the spectral gap that separates feasible from infeasible behaviors.
In full generality there exponentially many variables, but for Ising models, and in particularly ones with sparse interaction graphs, there are not so many coefficients and so this is simple.

## Slide 21: Can search on other “topologies”
We can put more constraints on our Polynomials
We only allow certain quadratic terms
Physical devices often have sparse interaction graphs
Input Bits
Output Bit
Fault Bit
Ancillary Bit

## Slide 22: Solving Binary Optimization Problems

## Slide 23: Standard Approaches
There are may classical Heuristic “local Search” methods
Greedy Search: flip the bit that reduces the penalty the most
  Gets stuck in local minima
TABU Search: Like greedy but uphill moves are allowed
  Previously visited states cannot be returned to
Simulated Annealing: Putative flip a random bit
  Accept the flip if the penalty is reduced
  Sometimes accept a penalty increase depending on a “temperature”
Notes: Putting all this together, we can compile circuit fault diagnosis behaviors of individual components into gap-optimal Ising models over any architecture.
Generally, there are no such Hamiltonians, and one will need to add ancillary bits (and this leads to additional challenges).
Here we see some sparse interaction graphs that support gap-optimal Ising Hamiltonians (where a priori we allow for a complete interaction graph).

## Slide 24: Physics-based solvers
Quantum Annealers use quantum effects to minimize energy
  have very restrictive topologies, so finding good mappings is often hard
Simulated Quantum Annealing: Monte-Carlo based on path-integrals
  Effectively simulates one type of quantum dynamics, but is quite slow
Parallel Tempering: Many Simultaneous runs of simulated annealing
  Different runs use different temperatures and can swap states
Substochastic Monte-Carlo: Monte Carlo approximation of Green’s function
  Exhibits the same tunneling behavior as quantum systems

## Slide 25: Benchmark problem
Fault diagnosis of Multiplier circuits of various widths.
Problem was proposed by IARPA

## Slide 26: Comparison of numerous solvers
Perdomo-Ortiz, et al., Phys. Rev. Appl. 12:1, 2019.

## Slide 27: Questions?

## Slide 28: Appendix: Circuit examples

## Slide 29: Basic examples
We target Hamiltonian architectures:
By convention we write
The “Stuck-at” fault behaviors both have optimal Gap :
noop and Not have optimal gap :

## Slide 30: Binary gates
The NOR (resp. AND, NAND, OR) have optimal gap
The xor (resp. xnor) needs an ancillary spin and has optimal gap :

## Slide 31: Adders
The half-adder and has optimal gap :
The Full Adder already studied surprisingly has Optimal gap :

## Slide 32: Adding Fault behaviors
We reverse what we did above and add fault bits.
  Here we use the common shorthand “>” to indicate a fault behavior.
The “conditional” Hamiltonian penalizes both and being set:
We bias against using faults via, for example, .

## Slide 33: Unary Gates with Faults
Note NOOP>SA0 (resp. NOOP>SA1, NOT>SA0, NOT>SA1) is essentially an or-gate.
Then noop>SA0>SA1 has optimal gap :
The Not>SA0>SA1 can be derived from this gate.