## Slide 1: Anaerobic Digestion
A primer
focused on failure
EWB-Purdue Design Team
Raymond Red Corn
Masters Student in Agricultural and Biological Engineering

## Slide 2: Failure; even on U.S.A. Farms
(Lusk, 1998)
Digester Type | % Inoperable
Complete Mix | 70
Plug Flow | 63
Covered Lagoon | 22

## Slide 3: Ground Rules
I welcome…
Interruptions
Additions
Tangents

## Slide 4: OUTLINE
Terminology
Digestion Overview
Opportunities in Wastewater
Loading Rate
VFAs in Anaerobic Digestion
How to Increase the Concentration of VFAs
Temperature
Markets for VFAs
Operational Advantages
Operational Challenges
Biogas
Objectives
Layout and Analysis

## Slide 5: Terminology

## Slide 6: Important term
Volatile Solid;
A solid which can be burned off; estimate of digestible organic matter.

## Slide 7: Volatile fatty acids
VFAs, Volatile Acids (VA),
Short Chain Fatty Acids (SCFA)
Organic Acids
Carboxylic Acid
Fatty Acid
(Aliphatic Tail)
Volatile Fatty Acids

## Slide 8: Different words ~ Same thing
Acetic Acid / Acetate
Deprotination
Propionic Acid/ Propionate
Butyric Acid/ Butyrate
Ammonium/ Ammonia
VFAs

## Slide 9: Overview of digestion
The role of acids and ammonia

## Slide 10: can it be digested?
Good
Human excretion
  Separate urine if possible
  Toilet paper OK
Animal excretion
Cooking grease
Food waste
Not Good
Woody material
Organic
(Volatile Solid)
Carbohydrate
Protein
Lipid

## Slide 11: It is complicated
Overall digestion Model
(Chen et. al., 2008, Batstone et al, 2002 and Tugtas, 2011)
Ammonia

## Slide 12: Digestion Rates vary
Different molecules; different rates
Carbohydrates
Proteins
Lipids
Simple Sugars
Starches
Cellulose/Fiber
Quickest
S l o w e s t
(Eastman and Ferguson, 1981)

## Slide 13
The most important factor
LOADING RATE

## Slide 14: Ideal loading
1.6 - 4.8 g VS/L/day
for single stage digestion
(Tchobanoglous et. al., 2003)

## Slide 15: Inhibition Happens at low levels
(Eastman and Ferguson, 1981), Acid inhibition level (Wang et. al, 2009), Ammonia inhibition (Chen et. al. , 2008)
Chart: VS Loading (g/L)
| 0 | 14 | 25 | 55
VA | 0 | 5 | 9 | 20
Ammonia | 0 | 4 | 7.5 | 17

## Slide 16: Stuck happens
Acids and ammonia smell bad
(Chen et. al., 2008, Bastone et al, 2002 and Tugtas, 2011)
Ammonia
Stuck Digester

## Slide 17: Design and implementation
Train and equip locals
for pH monitoring
Seed with sludge
from a working digester
Have a “stuck digester” plan

## Slide 18
…IT MATTERS
TEMPERATURE

## Slide 19: Temperature; many optimums
http://202.204.115.67/jpkch/jpkch/2008/wswx/chapter%206.htm
140˚F
102˚F

## Slide 20
Composition and treatment
BIOGAS

## Slide 21: BIOGAS; not just methane
Chart: 
| Carbon Dioxide | Other | Methane
Biogas | 30 | 5 | 65
(Tchobanglous et. al. ,2003)

## Slide 22: gas is not always methane
Especially at startup
(Mosey, 1983)
Acidogenesis
Glucose + 2H2O  2 Acetic + 2CO2 + 4H2
Glucose  Butyric + 2CO2 + 2H2
Glucose + 2H2  2 Propionic + 2H2O
Acetogenesis
Propionic + 2H2O Acetic + CO2
Butyric + 2H2O 2 Acetic + 2H2
Methanogenesis
Acetic  CH4 + CO2
CO2 + H2  CH4 + 2 H2O

## Slide 23: Startup can be confusing
Large amounts of gas will develop quickly. It may or may not be flammable but it is not necessarily methane.

## Slide 24: BIOGAS
Other Gases; N2, H2, H2O, H2S
H2S + 2O2  H2SO4
Control where this reaction occurs.
  Plan condensation points in piping
  Minor air sparging in digester
(Offgases)
(Soluble)

## Slide 25: Important points
Failure is common
Avoid failure by
  Managing loading, esp. food
  Managing sulfur behavior.
Appoint failure experts

## Slide 26
Laboratory of Renewable Resources Engineering

## Slide 27: References
Batstone, D.J., Keller, J., Angelidaki, I., Kalyuzhnyi, S., Pavlostathis, S., Rozzi, A., Sanders, W., Siegrist, H., Vavilin, V. 2002. The IWA Anaerobic Digestion Model No 1(ADM 1). Water Science & Technology, 45(10), 65-73.
Chen, Y., Cheng, J.J., Creamer, K.S. 2008. Inhibition of anaerobic digestion process: A review. Bioresource Technology, 99(10), 4044-4064.
Eastman, J.A., Ferguson, J.F. 1981. SOLUBILIZATION OF PARTICULATE ORGANIC-CARBON DURING THE ACID PHASE OF ANAEROBIC-DIGESTION. Journal Water Pollution Control Federation, 53(3), 352-366.
Lusk, P., Wiselogel, A. 1998. Methane recovery from animal manures: the current opportunities casebook. National Renewable Energy Laboratory Golden, CO.
Mosey, F.E. 1983. MATHEMATICAL-MODELING OF THE ANAEROBIC-DIGESTION PROCESS - REGULATORY MECHANISMS FOR THE FORMATION OF SHORT-CHAIN VOLATILE ACIDS FROM GLUCOSE. Water Science and Technology, 15(8-9), 209-232.
Tchobanoglous, G., Burton, F., Stensel, H. 2003. Wastewater Engineering; Treatment and Reuse. Fourth ed. McGraw Hill.
Tugtas, A.E. 2011. Fermentative Organic Acid Production and Separation. Marmara University.
Wang, Y., Zhang, Y., Wang, J., Meng, L. 2009. Effects of volatile fatty acid concentrations on methane yield and methanogenic bacteria. Biomass & Bioenergy, 33(5), 848-853.